## Slide 1: SCADA Mrs. Meera Ajit Khandekar Department of Instrumentation & Control College of Engineering, Pune

## Slide 4: SCADA HARDWARE:
On a more complex SCADA system there are essentially five levels or hierarchies:
• Field level instrumentation and control devices
• Marshalling terminals and RTUs
• Communications system
• The master station(s)
• The commercial data processing department computer system

## Slide 5: SCADA Software:

## Slide 9: SCADA Key Features: User Interface : • Keyboard • Mouse • Trackball • Touch screen Graphics Displays : • Customer-configurable, object orientated and bit mapped • Unlimited number of pages, • Resolution: up to 1280 x 1024 with millions of colors Alarms: • Client server architecture • Time stamped alarms to 1 millisecond precision (or better) • Single network acknowledgment and control of alarms • Alarms shared to all clients • Alarms displayed in chronological order • Dynamic allocation of alarm pages • User-defined formats and colors

## Slide 10: Trends: • Client server architecture • Export data to DBF, CSV files • X/Y plot capability • Event based trends • Trend gridlines or profiles • Background trend graphics • Real-time multi-pen trending RTU (and PLC) Interface: Interface also possible for RTUs, loop controllers, bar code readers and other equipment Driver toolkit available , Operates on a demand basis instead of the conventional predefined scan method • Optimization of block data requests to plcs • Rationalization of network user data requests • Maximization of PLC highway bandwidth

## Slide 11: Scalability Additional hardware can be added without replacing or modifying existing equipment. This is limited only by the PLC architecture (typically 300 to 40,000 points) Access to Data • Direct, real-time access to data by any network user • Third-party access to real-time data, e.g. Lotus 123 and EXCEL • network DDE • DDE compatibility: read, write and exec • DDE to all IO device points • Clipboard

## Slide 12: Database • ODBC driver support • Direct SQL commands or high level reporting Networking Supports all netbios compatible networks such as netware, LAN manager, windows for workgroups, windows NT (changed from existing NT) • Support protocols netbeui, IPX/SPX, TCP/IP and more • Centralized alarm, trend and report processing - data available from anywhere in the network • dual networks for full LAN redundancy

## Slide 13: Fault Tolerance and Redundancy • Dual networks for full LAN redundancy • Redundancy that can be applied to specific hardware • Supports primary and secondary equipment configurations • Intelligent redundancy allows secondary equipment to contribute to processing load • Automatic changeover and recovery Client/Server Distributed Processing • Open architecture design • Real-time multitasking • Client/server fully supported with no user configuration • Distributed project updates (changes reflected across network) • Concurrent support of multiple display nodes • Access any tag from any node • Access any data (trend, alarm, report) from any node

## Slide 14: Thank you!!!